## Slide 1
SOFTWARE DEFINED RADIO
From Bits to Airwaves
A live demo with GNU Radio Companion, a HackRF One, and a 144/440 MHz handheld
Mark Grennan • W5TSU • 2026

## Slide 2
BEFORE WE TOUCH THE RADIO
The Airwaves: 3 Hz – 3 THz
By international convention (ITU), everything humans use for wireless communication -- from submarine navigation to satellite links -- lives somewhere in this range. Twelve decades, back to back, and every one of them is already spoken for.
ELF
SLF
ULF
VLF
LF
MF
HF
VHF
UHF
SHF
EHF
THF
3 Hz
3 THz
Each band spans one decade -- band N runs 0.3×10ᴺ Hz to 3×10ᴺ Hz.
Tonight lives here: VHF / UHF
• 2m (144-148 MHz) and 70cm (420-450 MHz) -- our ham bands -- plus FM broadcast (88-108 MHz), all three narrow slivers of one 270:1 span (30 MHz-3 GHz).
ITU Radio Regulations, Article 2 -- band designations ELF-THF
1 / 19

## Slide 3
BEFORE WE TOUCH THE RADIO
Every Signal Arrives Already Mixed With Noise
Noise From Nature
• Thermal noise: the atoms in your receiver's own components are vibrating with heat -- that's noise, before an antenna is even involved.
• Modeled as Gaussian / "white" noise -- flat across the whole band. That's the hiss you hear with nothing tuned in.
• Lightning sferics: crackly pops from distant thunderstorms, audible from VLF up through HF.
• Ionized meteor trails briefly reflect distant signals into a receiver -- noise and signal from the same natural event.
Noise We Make Ourselves
• Every switching power supply, phone charger, and LED driver in this room is radiating RF -- one of the most common interference sources hams fight.
• USB 3.0 leaks clock noise at multiples of 480 MHz; HDMI cables can splatter interference across roughly 148-742 MHz.
• Monitors, DisplayPort, powerline networking adapters -- all of it adds more.
• None of it is malicious. It's just what happens when fast digital clocks run next to a receiver.
Every demo tonight starts here: find the signal you want inside everything else that's already there. Watch the noise floor on the very first demo -- it's not empty.
Sources: pysdr.org (Ch. 10, Noise and Random Variables) and sigidwiki.com (Interfering Emissions category)
2 / 19

## Slide 4
THE IDEA
What Is Software Defined Radio?
• Traditional radios: filtering, mixing, and demodulation are done by dedicated analog/digital hardware built for one job.
• SDR: an antenna feeds a wideband ADC/DAC, and everything after that -- tuning, filtering, demodulating, decoding -- happens in software.
• Same box, endless radios: change the software, not the hardware.
• Today's demo does this literally -- one HackRF, six different “radios,” just by loading a different flowgraph.
Antenna
Analog RF in/out
ADC / DAC (HackRF)
Samples ↔ RF
Software (GNU Radio)
Filter · demod · decode
SDR Demo -- GNU Radio + HackRF + Ham Handheld
3 / 19

## Slide 5
THE HARDWARE
HackRF One
Core Specs
• 1 MHz – 6 GHz tuning range
• Up to 20 Msps, 8-bit quadrature ADC/DAC (8-bit I, 8-bit Q)
• Half-duplex (RX or TX, never both at once)
• Hi-Speed USB 2.0, USB-powered, open source hardware
• This talk: driven via SoapySDR from GNU Radio
TX Capabilities
• Two software-controlled TX gain stages -- no physical knobs: an on/off RF amp (~+11 dB) and a VGA/IF gain stage, 0-47 dB in 1 dB steps.
• Max output power varies with frequency -- roughly +5 to +15 dBm from 1 MHz-2.17 GHz, dropping to about 0-10 dBm up through 4 GHz. Best performance is actually 2170-2740 MHz.
• Tonight's TX demos default to just 10 dB of VGA gain -- comfortably at the low end, per the "minimum power necessary" guidance.
• No built-in per-band TX filtering -- it's a general-purpose transmitter, so staying inside our allocated ham segments is on us.
Sources: hackrf.readthedocs.io, greatscottgadgets.com/hackrf/one
4 / 19

## Slide 6
THE SOFTWARE
GNU Radio + GNU Radio Companion
• GNU Radio: open-source DSP toolkit -- filters, modulators, demodulators, resamplers, all as reusable building blocks.
• GNU Radio Companion (GRC): drag-and-drop flowgraph editor that generates the underlying Python for you.
• SoapySDR: hardware abstraction layer -- the same flowgraph blocks work whether it's a HackRF, RTL-SDR, LimeSDR, or others.
• Every flowgraph in this demo is a plain-text .grc file -- versionable, diffable, shareable.
Toolchain
Flowgraph (.grc)
GNU Radio Companion
Generated Python
GNU Radio runtime + SoapySDR
HackRF One
SDR Demo -- GNU Radio + HackRF + Ham Handheld
5 / 19

## Slide 7
CORE CONCEPT
Reading a Flowgraph
• Blocks are connected left to right: a Source produces samples, middle blocks process them, a Sink consumes them.
• Everything on the RF side flows as complex IQ samples -- one number for signal strength/phase in two dimensions (I and Q), captured at the sample rate.
• Sample rate sets your instantaneous bandwidth: capture at 6 Msps and you're watching 6 MHz of spectrum at once, not just one channel.
HackRF Source
Filter / Resample
Demodulate
Audio / File Sink
SDR Demo -- GNU Radio + HackRF + Ham Handheld
6 / 19

## Slide 8
DEMO 0 · ICEBREAKER
FM Broadcast Receiver
RECEIVE ONLY
• Flowgraph: 06_bonus_fm_broadcast_receiver.grc
• Tune to any strong local FM station (88-108 MHz) and hear music instantly through the laptop speakers.
• Not a ham-band demo -- it's here to prove the whole chain works (driver, HackRF, GNU Radio, audio out) before the ham material, and it needs no license to receive.
SDR Demo -- GNU Radio + HackRF + Ham Handheld
7 / 19

## Slide 9
DEMO 1
Live Spectrum & Waterfall
RECEIVE ONLY
• Flowgraph: 01_spectrum_waterfall_tunable.grc
• One flowgraph, both ham bands -- retype the center frequency live: 146.520 MHz (2m) then 446.000 MHz (70cm).
• Key up the handheld on each band and watch the signal light up the spectrum plot and waterfall in real time.
• Talking point: this is the same 10 MHz of RF spectrum a traditional radio can only look at one narrow slice of at a time.
SDR Demo -- GNU Radio + HackRF + Ham Handheld
8 / 19

## Slide 10
DEMO 2
Tunable NBFM Voice Receiver
RECEIVE ONLY
• Flowgraph: 02_nbfm_voice_receiver.grc
• A real narrowband FM voice receiver -- channel filter, resampler, FM demodulator, straight to the speakers.
• Default: 146.520 MHz, the national 2m simplex calling frequency. Key up the handheld there and it comes through the laptop.
• Talking point: this whole receiver -- the part that's a dedicated chip in a normal radio -- is about a dozen blocks of software here.
SDR Demo -- GNU Radio + HackRF + Ham Handheld
9 / 19

## Slide 11
DEMO 3 · THE HEADLINE DEMO
Record the Entire 2m Band
• Flowgraph: 03_record_2m_band_to_file.grc
• Tunes to 146.0 MHz center at 6 Msps -- covers 143.0 to 149.0 MHz, the whole 144-148 MHz 2m band with margin to spare.
• Not one channel -- every signal on the entire band, captured at once
  – Raw IQ, written to a self-describing file (sample rate + center frequency saved in the header)
• Live: hit Execute, key up the handheld once or twice, hit Stop. ~2.9 GB/minute -- a 20-30 second capture is plenty for the demo.
SDR Demo -- GNU Radio + HackRF + Ham Handheld
10 / 19

## Slide 12
DEMO 3B · THE PAYOFF
...And Play It Back Over the Air
TRANSMITS — SEE NEXT SLIDE
• Flowgraph: 04_playback_2m_band_from_file.grc
• Reads the file back and feeds it straight into the HackRF's transmitter -- the exact recorded band reappears on the air.
• Watch the waterfall reproduce exactly what was captured; the handheld hears the same signal a second time, live.
• This is the moment that makes SDR click: the recording *is* the radio signal -- numbers on disk, transmitted back as RF.
SDR Demo -- GNU Radio + HackRF + Ham Handheld
11 / 19

## Slide 13
⚠ BEFORE WE TRANSMIT
Part 97 Ground Rules
• A licensed control operator is present the entire time we transmit.
• We identify with callsign at the start/end and every 10 minutes.
• No music, no broadcast content -- a brief, identified test transmission only.
• Power stays at the minimum needed -- TX gain starts low and only comes up as far as the demo needs.
• No control operator today, or want zero on-air emission? The HackRF TX port can go into a dummy load instead of an antenna -- same demo, nothing radiated.
SDR Demo -- GNU Radio + HackRF + Ham Handheld
12 / 19

## Slide 14
DEMO 4 · OPTIONAL
NBFM Voice Transmitter
TRANSMITS — CONTROL OP REQUIRED
• Flowgraph: 05_nbfm_voice_transmitter.grc
• The reverse direction: laptop microphone → NBFM modulator → HackRF → antenna.
• Talk into the laptop, hear yourself on the handheld -- live two-way, same 146.520 MHz simplex frequency as Demo 2.
• Skip this one if there's no control operator in the room -- Demos 0-3 already tell the full story.
SDR Demo -- GNU Radio + HackRF + Ham Handheld
13 / 19

## Slide 15
RECAP
What Just Happened, Technically
• One piece of hardware -- the same HackRF -- was an FM radio, a spectrum analyzer, a repeater receiver, a wideband recorder, and a voice transceiver, in the same 20 minutes.
• The only thing that changed between demos was which flowgraph was loaded -- no soldering, no new hardware.
• The recording in Demo 3 wasn't a simulation of the 2m band -- it was the actual RF, represented as numbers, played back as actual RF.
• That's the whole idea of “software defined”: the radio is defined by the software running on general-purpose hardware, not by purpose-built circuitry.
SDR Demo -- GNU Radio + HackRF + Ham Handheld
14 / 19

## Slide 16
WHERE THIS GOES NEXT
More Demo Ideas
Quick wins
• CTCSS/PL tone squelch decode
• CW (Morse) ID transmitter
• RDS decode from FM broadcast
• APRS decode (144.390 MHz)
Bigger swings
• WSPR / FT8 weak-signal decode
• ADS-B aircraft tracking (1090 MHz)
• Cross-band digital repeater
• Digital voice (DMR / D-STAR) decode
Full writeup with effort/dependency notes: BRAINSTORM.md
SDR Demo -- GNU Radio + HackRF + Ham Handheld
15 / 19

## Slide 17
REFERENCE
Specs at a Glance
Frequency range
1 MHz – 6 GHz (HackRF One)
Sample rate used today
2–10 Msps depending on demo
2m band
144.000 – 148.000 MHz
70cm band
420.000 – 450.000 MHz
2m simplex calling freq
146.520 MHz
Demo 3 capture
146.0 MHz center @ 6 Msps ≈ 2.9 GB/min
HackRF TX power (typical)
≈ 10–15 dBm max, kept low for these demos
SDR Demo -- GNU Radio + HackRF + Ham Handheld
16 / 19

## Slide 18
RESOURCES
Go Build Something
• GNU Radio
  – gnuradio.org — the toolkit, docs, and tutorials
• HackRF One
  – greatscottgadgets.com/hackrf — hardware + firmware
• SoapySDR
  – github.com/pothosware/SoapySDR — the hardware abstraction layer used today
• ARRL
  – arrl.org — licensing info and Part 97 reference
• This kit
  – All flowgraphs, README, and brainstorm doc are in this repo’s flowgraphs/ and top-level README.md / BRAINSTORM.md
SDR Demo -- GNU Radio + HackRF + Ham Handheld
17 / 19

## Slide 19
Thank You
Questions? Let's get on the air.
Mark Grennan • W5TSU • mark@grennan.com